## Slide 1
Group C5
Tug Fork River
Fecal Coliform Water Quality Calibration Plots
November 4, 2021
The TMDL model was run under baseline conditions with nonpoint sources, NPDES permitted point sources, CSO discharges, and failing septic systems represented at 100% of loading rates.

## Slide 2
Watershed Characteristics for Calibration Plot Streams
SUBID | Stream Name | Stream Size | Point Sources | Nonpoint Sources
100 | Tug Fork | Very Large | Package plant, HAU | Failing septics, residential
153 | Tug Fork | Very Large | Package plant, HAU | Failing septics, residential
185 | Tug Fork | Very Large | Package plant, HAU | Failing septics, residential
293 | Tug Fork | Very Large | Package plant, HAU | Failing septics, residential
1004 | Mill Creek | Medium | Package plant, HAU | Pasture, riparian pasture, failing septics, residential
1011 | Vinson Branch | Very Small | None | Failing septics, residential
1028 | Bull Creek | Small | None | Failing septics, residential
2003 | Pigeon Creek | Large | Package plant, HAU, mining bath house | Failing septics, residential
2041 | Trace Fork | Medium | Package plant, HAU, mining bath house, POTW | Pasture, failing septics, residential
2106 | Slick Rock Branch | Very Small | None | Failing septics, residential
3007 | Peg Fork | Small | None | Background only
3026 | Mate Creek | Medium | None | Failing septics, residential
3066 | Ben Creek | Medium | Mining bath house | Failing septics, residential
4014 | Panther Creek | Large | Package plant | Pasture, failing septics, residential
4037 | Tug Fork | Very Large | None | Failing septics, residential
4042 | War Branch | Small | None | Failing septics, residential
5001 | Dry Fork/Tug Fork | Large | Package plant, HAU, POTW | Failing septics, residential
5033 | Little Slate Creek | Small | None | Failing septics, residential
5058 | Big Creek | Medium | None | Pasture, failing septics, residential
5077 | Jacobs Fork | Medium | None | Failing septics, residential
6010 | Snipe Branch | Small | None | Failing septics, residential

## Slide 3
Watershed Characteristics for Calibration Plot Streams (continued)
SUBID | Stream Name | Stream Size | Point Sources | Nonpoint Sources
6016 | Clear Fork | Small | POTW | Failing septics, residential
6019 | Tug Fork | Large | Package plant, HAU | Failing septics, residential
6040 | Hensley Creek | Small | None | Failing septics, residential
6055 | Tug Fork | Large | Package plant, POTW, CSO | Failing septics, residential
6062 | Elkhorn Creek | Large | Package plant, HAU | Failing septics, residential
6089 | North Fork/Elkhorn Creek | Medium | Package plant | Failing septics, residential
6107 | Tug Fork | Large | POTW | Failing septics, residential
6116 | Mitchell Branch | Small | None | Failing septics, residential
6144 | Harmon Branch | Small | None | Residential
6160 | Spice Creek | Small | None | Failing septics, residential
6179 | Tug Fork | Medium | None | Failing septics, residential
6192 | UNT/Tug Fork RM 152.09 | Very Small | None | Failing septics, residential
6199 | Puncheoncamp Branch | Small | None | Failing septics, residential
6206 | Millseat Branch | Small | None | Failing septics, residential
6207 | Tug Fork | Small | None | Failing septics, residential
6212 | Sams Branch | Small | None | Failing septics, residential