## Slide 1
TMDL Development
Hughes River Watershed
May 15, 2014

## Slide 2: Agenda
Background information on Water Quality Standards, impaired waters and TMDLs
Brief history of WV TMDL development
Overview of WVDEP’s TMDL process
Discussion of local impaired waters and their TMDL timeline
Pre-TMDL Monitoring Plan for local waters
Discussion – Free form questions and answers

## Slide 3: What’s a TMDL?
“Total Maximum Daily Load” – How much of a pollutant/s a stream can receive and remain healthy
TMDL development is required by Clean Water Act for all impaired streams
TMDL is a pollutant budget – prescribes reduction in pollutants that result in the restoration of an impaired stream

## Slide 4: What’s an impaired stream?
Stream that doesn’t meet water quality standards
West Virginia Water Quality Standards are codified in 47 CSR 2
Standards include designated uses for WV waters and water quality criteria to protect those uses
Criteria can be numeric or narrative
Impaired streams (streams that are not meeting criteria) are on the 303(d) List

## Slide 5: Numeric Criteria
Human Health Protection
  Fecal Coliform bacteria (Water Contact)
    200 counts/100ml as a monthly geometric mean
    no more than 10% of samples in a month exceed 400 counts/100ml
Human Health/Aquatic Life Protection
  Total Iron
    1.5 mg/l as a 4 day average concentration (warmwater)
    Not to be exceeded more than once every 3 years

## Slide 6: Narrative Criteria
Biological Impairment
  Conditions Not Allowable in State Waters
  (47 CSR 2-3.2i) “.....no significant adverse impact to the chemical, physical, hydrologic or biological components of aquatic ecosystems shall be allowed.”

## Slide 7: Previous 47 CSR 2 - 3.2.i Assessment
Based on Benthic Macroinvertebrates
West Virginia Stream Condition Index (WVSCI)
  Standardized method for assessing benthic macroinvertebrates (aquatic bugs)
  WVSCI stream scores normalized to 0 - 100 range
  Streams scoring less than the 60.6 threshold value labeled as “impaired” and placed on the 303(d) list
  Streams listed as impaired slated for TMDLs
  “Biologically Impaired” streams evaluated for source/s of impairment during the TMDL development process (Stressor Identification Process)

## Slide 8: 2012 Legislative Changes
Senate Bill 562 passed by 2012 the West Virginia Legislature amended the WV Water Pollution Control Act
Requires “evaluation of the holistic health of the aquatic ecosystem”
Requires DEP to develop and secure legislative approval of new rules to interpret 47 CSR 2-3.2.i
http://www.legis.state.wv.us/wvcode/ChapterEntire.cfm?chap=22&art=11
Notes: Web link is cumbersome – may want to have a dozen or so copies to hand out

## Slide 9: Biological Impairment Path Forward
DEP currently working to develop a methodology which meets the legislative requirements set forth in SB562; considering incorporating fish assessments
WV Draft 2012 303(d) List contained no new bio listings
No new WV developed TMDLs until new methodology effective
Will continue benthic/fish monitoring in interim
  Likely to remain a component of new method
  May be able to address existing 303(d) listings if stream no longer impaired per WVSCI or if WVSCI stressors can be resolved by attainment of numeric criterion

## Slide 10: West Virginia TMDL History
TMDL development required by Clean Water Act for all impaired streams
If State doesn’t develop TMDLs, EPA must
WV couldn’t (resources), EPA didn’t
EPA was sued in 1995, settled suit by entering into consent decree with plaintiffs, and began developing WV TMDLs
In 2004, WV finalized its first group of TMDLs developed under state direction

## Slide 11: WVDEP TMDL Process
Stream Selection
Pre-TMDL monitoring, source identification and characterization
Contract to model water quality and hydrology
Allocation development
Report development
Finalization

## Slide 12: Process Highlights
Synchronized with WV Watershed Management Framework
48 month process (Stream selection – EPA approval)
Multiple opportunities for public outreach/ stakeholder input
Pre-TMDL water quality monitoring
Source identification and characterization

## Slide 13: TMDL Stream Selection Process
Spread development over State
Evaluate list of impaired waters
Consider WMF
Maximize efficiency
  focus geographically
  address all known or suspected impairments
Resources

## Slide 14: TMDL Development Stream Selection Process
Watershed Management Framework Consideration
Within HG D3 candidate watersheds = Greenbrier, James, Little Kanawha, Lower New, Monongahela, Upper New
TMDL Development Hydrologic Group D3

## Slide 15: TMDL Development Stream Selection Process
Statewide Coverage Considerations
  DEP TMDL development has occurred in Greenbrier, James, New and Monongahela watersheds.
  Hughes River mainstem and selected tributaries on the current 303d list

## Slide 17: TMDL Development Stream Selection Process
DEP proposed TMDL development for Monongahela Mainstem, Unt/Deckers Creek RM 18.48 and Hughes River watersheds.
DEP advertised proposal and provided opportunity for comment February 27 through March 28 - No Comments received.
Final selection – Monongahela River mainstem, Unt/Deckers Creek RM 18.48 and Hughes River watersheds.
TMDLs will be developed for any new impairments identified in pre-TMDL monitoring

## Slide 18: HG D3 TMDL Timeline
Stream selection
2/14 – 3/14
Monitoring plan development
3/14 - 4/14
Outreach (TMDL process + monitoring plan specifics)
5/14 – 6/14
Stream Monitoring and Source Tracking
7/14 – 6/15

## Slide 19: HG D3 TMDL Timeline
Modeling
10/15 – 6/16
Outreach (Status Update)
7/16 - 9/16
Draft TMDLs (Internal Review)
3/17
Outreach (PN/PC on Drafts)
4/17 – 6/17

## Slide 20: HG D3 TMDL Timeline
Finalization (including EPA approval) 12/17
Implementation begins
7/18 – NPDES Water Permits
1/19 – NPDES Mining Permits

## Slide 21: Pre-TMDL Monitoring Plan
Goal – to generate robust/ recent data to:
  Make accurate impairment assessments
  Calibrate watershed models
  Quantify the impacts of significant pollutant sources
Today’s presentation is a preliminary plan; to be refined via WVDEP field recon and stakeholder input

## Slide 22: Pre-TMDL Monitoring Plan
Monitoring period = July 2014 – June 2015
Sampling frequency
  Water chemistry (monthly)
  Flow measurement (selected locations, monthly)
  Benthic macroinvertebrates (once )
  Fish (once at sites meeting sampling protocol)
  RBP habitat evaluations (once )
Notes: If asked about monthly chemistry parameters answer that it varies with the prescribed sampling suites (whitman’s one pager)
If asked why do TDS ions – answers are 1) document current conditions and 2)use in stressor ID for benthics

## Slide 23: Pre-TMDL Monitoring Plan
Detailed map on DEP webpage - GIS available
Impairment/potential impairment sampling suites:
  Fecal - fecal coliform
  Mn - Manganese
  Sed – TSS, T. & Dis. Iron
  Ion – Alkalinity, Barium, Boron, Bromide, Calcium, Chloride, Manganese, Potassium, Sodium, Strontium, Sulfate, TDS, TKN,
  Comp – Alkalinty, Dis. & Tot. Aluminum, Barium, Boron, Bromide, Calcium, Cholride, Dis. Copper, Fecal, Dis. & Tot. Iron, Manganese, NO2-NO3, Tot. Orthophosphate, Dis. & Tot. Phosphorus, Potassium, Tot. Selenum, Sodium, Strontium, Sulfate, TDS, TKN, TSS and Dis. Zinc.
  PRS - Comp + Hot Acidity
  Bio - aquatic bug collection (fish at sites meeting sampling protocol)
  190 sites on 148 streams

## Slide 25: Source Tracking Efforts
Limits of POTW collection systems
Assessment of failing onsite systems
AFOs, Livestock counts, livestock stream access
Riparian zone condition
Unmapped road density
Qualitative assessment of sediment sources
Active Mining Point Source Info
Abandoned Mine Lands

## Slide 26: Stakeholder Input
General comments regarding plan’s adequacy in addressing goals
Does the plan provide for monitoring of particularly bad or good streams that you know about?
Does the plan provide monitoring sufficient to characterize significant pollutant sources?
Do you have water quality data to contribute?

## Slide 27: Future Input Opportunities
Public Meeting to present Draft TMDL and formal Public Notice/Public Comment
– Spring 2017
Public meeting to present TMDL status update
– Summer 2016

## Slide 28: WVDEP Contact Information
Contact: Steve Young – Stephen.A.Young@wv.gov
Tele: (304) 926-0499 Ext 1042;
FAX: (304) 926-0496
601 57th Street SE, Charleston WV 25304
www.dep.wv.gov
  Select Water and Waste Home
  On left select Watershed Management, click on “ Total Maximum Daily Load”

## Slide 29
Questions???