## Slide 1
TMDL Development
Tygart Valley River Watershed
May 9th & 10th 2012
WV DEP
James Laine

## Slide 2: Agenda
Background information on Water Quality Standards, impaired waters and TMDLs
Brief history of WV TMDL development
Overview of WVDEP’s TMDL process
Discussion of local impaired waters and their TMDL timeline
Pre-TMDL Monitoring Plan for local waters
Discussion – Free form questions and answers

## Slide 3: What’s a TMDL?
“Total Maximum Daily Load” – How much of a pollutant/s a stream can receive and remain healthy
TMDL development is required by Clean Water Act for all impaired streams
TMDL is a pollutant budget – prescribes reduction in pollutants that result in the restoration of an impaired stream

## Slide 4: What’s an impaired stream?
Stream that doesn’t meet water quality standards
West Virginia Water Quality Standards are codified in 47 CSR 2
Standards include designated uses for WV waters and water quality criteria to protect those uses
Criteria can be numeric or narrative
Impaired streams (streams that are not meeting criteria) are on the 303(d) List

## Slide 5: Numeric Criteria
Human Health Protection
  Fecal Coliform bacteria (Water Contact)
    200 counts/100ml as a monthly geometric mean
    no more than 10% of samples in a month exceed 400 counts/100ml
Human Health/Aquatic Life Protection
  Total Iron
    1.5 mg/l as a 4 day average concentration (warmwater)
    1.0 mg/l as a 4 day average concentration (troutwater)
    Not to be exceeded more than once every 3 years

## Slide 6: Numeric Criteria
Human Health
  Total Manganese
    1.0 mg/l (Human Health) drinking water
    Effective within a 5 mile zone above a public intake
Aquatic Life
  Dissolved Aluminum
    750 ugl/l as a 4 day avg. concentration (warmwater) 87 ug/l as a 4 avg. concentration (troutwater)
    Not to be exceeded more than once every 3 years

## Slide 7: Narrative Criteria
Biological Impairment
  Conditions Not Allowable in State Waters
  (47 CSR 2-3.2i) “.....no significant adverse impact to the chemical, physical, hydrologic or biological components of aquatic ecosystems shall be allowed.”

## Slide 8: Previous 47 CSR 2 - 3.2.i Assessment
Based on Benthic Macroinvertebrates
West Virginia Stream Condition Index (WVSCI)
  Standardized method for assessing benthic macroinvertebrates (aquatic bugs)
  WVSCI stream scores normalized to 0 - 100 range
  Streams scoring less than the 60.6 threshold value labeled as “impaired” and placed on the 303(d) list
  Streams listed as impaired slated for TMDLs
  “Biologically Impaired” streams evaluated for source/s of impairment during the TMDL development process (Stressor Identification Process)

## Slide 9: Recent Legislative Changes
Senate Bill 562 passed by 2012 the West Virginia Legislature amended the WV Water Pollution Control Act
Requires “evaluation of the holistic health of the aquatic ecosystem”
Requires DEP to develop and secure legislative approval of new rules to interpret 47 CSR 2-3.2.i
http://www.legis.state.wv.us/Bill_Text_HTML/2012_SESSIONS/RS/pdf_bills/SB562%20SUB1%20enr%20PRINTED.pdf
Notes: Web link is cumbersome – may want to have a dozen or so copies to hand out

## Slide 10: Biological Impairment Path Forward
DEP currently working to develop a methodology which meets the legislative requirements set forth in SB562; considering incorporating fish assessments
No new 303(d) listings under old methodology
No new TMDLs until new methodology effective
Will continue benthic monitoring in interim
  Likely to remain a component of new method
  May be able to address existing 303(d) listings if stream no longer impaired per WVSCI or if WVSCI stressors can be resolved by attainment of numeric criterion

## Slide 11: West Virginia TMDL History
TMDL development required by Clean Water Act for all impaired streams
If State doesn’t develop TMDLs, EPA must
WV couldn’t (resources), EPA didn’t
EPA was sued in 1995, settled suit by entering into consent decree with plaintiffs, and began developing WV TMDLs
In 2004, WV finalized its first group of TMDLs developed under state direction

## Slide 12: WVDEP TMDL Process
Stream Selection
Pre-TMDL monitoring, source identification and characterization
Contract to model water quality and hydrology
Allocation
Report development
Finalization

## Slide 13: Process Highlights
Synchronized with WV Watershed Management Framework
48 month process (Stream selection – EPA approval)
Multiple opportunities for public outreach/ stakeholder input
Pre-TMDL water quality monitoring
Source identification and characterization

## Slide 14: TMDL Stream Selection Process
Spread development over State
Evaluate list of impaired waters
Consider WMF
Maximize efficiency
  focus geographically
  address all known or suspected impairments
Resources

## Slide 15: Watershed Management Framework
32 watersheds (8-digit HUC)
5 Hydrologic Groups (A – E)
Geographical way to organize water resource management – Within DEP, watershed assessment, NPDES Permit reissuance and nonpoint source project funding synchronized
WVDEP TMDL development synchronized

## Slide 16: TMDL/WMF Synchronization
Pre-TMDL monitoring occurs concurrently with WMF assessment year
TMDL completion six months prior to start of WMF implementation year
5yr WMF cycle/15 year plan
3 bites at each HG apple

## Slide 17: TMDL Development Stream Selection Process
Watershed Management Framework Consideration
Within HG B3, candidate watersheds = Coal, Elk, Lower Kanawha, North Branch Potomac, Tygart Valley
TMDL Development Hydrologic Group B3

## Slide 18: TMDL Development Stream Selection Process
Statewide Coverage Considerations
  DEP TMDL development has occurred in Coal, Elk, Lower Kanawha and North Branch Potomac watersheds.
  Significant number of Tygart streams/impairments on the 303d list; EPA-developed TMDLs for the Tygart Valley watershed need revision due to changes in aluminum and manganese water quality standards

## Slide 19: TMDL Development Stream Selection Process
DEP proposed TMDL development in Tygart Valley River watershed
DEP advertised proposal and provided opportunity for comment (March 7 – April 13, 2012) - No Comments received
Final selection – Tygart Valley River and tributaries from headwaters to its confluence with the Monongahela River

## Slide 20: TMDL Development Stream Selection Process
Address all 2010 303(d) listings except PCBs in Tygart Valley Lake. New data indicates a non-impaired condition and delisting will be proposed in draft 2012 303(d) list
2001 EPA TMDLs will also be re-evaluated during this effort
TMDLs will be developed for any new impairments identified in pre-TMDL monitoring (with possible exception of Bio Impairment)

## Slide 24: HG B3 TMDL Timeline
Stream selection
3/12 – 4/12
Monitoring plan development
3/12 - 5/12
Outreach (TMDL process + monitoring plan specifics)
5/12 – 6/12
Stream Monitoring and Source Tracking
7/12 – 6/13

## Slide 25: HG B3 TMDL Timeline
Modeling
10/13 – 6/14
Outreach (Status Update)
7/14 - 9/14
Draft TMDLs (Internal Review)
3/15
Outreach (PN/PC on Drafts)
4/15 – 6/15

## Slide 26: HG B3 TMDL Timeline
Finalization (including EPA approval) 12/15
Implementation begins
7/16 – NPDES Water Permits
1/17 – NPDES Mining Permits

## Slide 27: Pre-TMDL Monitoring Plan
Goal – to generate robust/ recent data to:
  Make accurate impairment assessments
  Calibrate watershed models
  Quantify the impacts of significant pollutant sources
Today’s presentation is a preliminary plan; to be refined via WVDEP field recon and stakeholder input

## Slide 28: Pre-TMDL Monitoring Plan
Detailed map on DEP webpage
Impairments/potential impairments being evaluated:
  Biological Integrity (bug collection for reevaluation of stream status)
  Total Iron, Dissolved Aluminum, Total Manganese, pH
  Fecal coliform bacteria
  336 sites on 227 streams
GIS coverage available upon request

## Slide 29
Legend
ACID RAIN
ACID RAIN/AMD
ACID RAIN/AMD/FECAL
ACID RAIN/AMD/FECAL/BIO
ACID RAIN/AMD/FECAL/Be/Se/BIO
ACID RAIN/BIO
ACID RAIN/FECAL/BIO
ACID RAIN/SED
ACID RAIN/SED/BIO
ACID RAIN/SED/Be/Se
ACID RAIN/SED/FECAL
ACID RAIN/SED/FECAL/BIO
ACID RAIN/SED/FECAL/Be/Se/BIO
AMD
AMD/FECAL
AMD/FECAL/BIO
AMD/FECAL/Be/Se/BIO
AMD/FECAL/ION/BIO
AMD/FECAL/ION/Be/Se
AMD/FECAL/ION/Be/Se/BIO
AMD/FECAL/ION/Be/Se/Mn/BIO
AMD/FECAL/ION/Mn
AMD/FECAL/ION/Mn/BIO
AMD/FECAL/Mn/BIO
AMD/FECAL/NUTRIENT/ION/BIO
AMD/FECAL/NUTRIENT/ION/Mn
AMD/FECAL/NUTRIENT/ION/Mn/BIO
CONTROL/BIO
CONTROL/PRS-BIO
SED/FECAL
SED/FECAL/BIO
SED/FECAL/ION/BIO
SED/FECAL/Mn/BIO
SED/FECAL/NUTRIENT
SED/FECAL/NUTRIENT/BIO

## Slide 31
Notes: Should explain sampling suite legend i.e what does “AMD” mean? Would be nice to include Whitman’s one pager showing parameters monitored in each suite.

## Slide 32: Pre-TMDL Monitoring Plan
Monitoring period = July 2012 – June 2013
Sampling frequency
  Water chemistry (monthly)
  Flow measurement (selected locations, monthly)
  Benthic macroinvertebrates (once in WVSCI Index period)
  RBP habitat evaluations (once with benthic assessment)
Notes: If asked about monthly chemistry parameters answer that it varies with the prescribed sampling suites (whitman’s one pager)
If asked why do TDS ions – answers are 1) document current conditions and 2)use in stressor ID for benthics

## Slide 33: Source Tracking Efforts
Abandoned Mine Lands
Limits of POTW collection systems
AFOs, Livestock counts
Riparian zone condition
Unmapped road density
Qualitative assessment of sediment sources
Active Mining Point Source Info

## Slide 34: Stakeholder Input
General comments regarding plan’s adequacy in addressing goals
Does the plan provide for monitoring of particularly bad or good streams that you know about?
Does the plan provide monitoring sufficient to characterize significant pollutant sources?
Do you have water quality data to contribute?

## Slide 35: Future Input Opportunities
Public Meeting to present Draft TMDL and formal Public Notice/Public Comment
– Spring 2015
Public meeting to present TMDL status update
– Summer 2014

## Slide 36: WVDEP Contact Information
Contact: Steve Young – Stephen.A.Young@wv.gov
Tele: (304) 926-0499 Ext 1042;
FAX: (304) 926-0496
601 57th Street SE, Charleston WV 25304
www.dep.wv.gov
  Select Water and Waste Home
  On left select Watershed Management, click on “ Total Maximum Daily Load”

## Slide 37
Questions???