## Slide 1: WV E4 Water Quality Calibration
Fe and TSS
Twelvepole, Big Sandy, Lower Ohio Watersheds

## Slide 2: Calibration
Ran hourly 2016 - 2017
Assigned Calibration Levels
  1 – Headwater, impaired
  2 – Downstream, impaired
  3 – Headwater, unimpaired (basically calibrating background – no WAB hits)
  4 – Downstream, unimpaired (not helpful – no WAB hits to calibrate to)
  No Data – no calibration data
Calculated dominant disturbance for each sub

## Slide 3: Landuses
Lower Ohio
  No mining
  Agriculture – Pasture dominates frequently (25-45%)
  Some big harvested areas
  Urban/Residential – low level throughout
Big Sandy
  Only WQ mining – does not dominate anywhere
  Urban/Residential – Several subs over 25%
  Agriculture – quite a bit
  Some big harvested areas
Twelvepole
  TCH and WQ mining
  Urban/Residential – substantial – 100% urban/res sws (unimpaired, downstream sub so hard to calibrate)
  Lot of undisturbed mining
  Big harvest jobs
  Agriculture – not a lot, one 20%

## Slide 4: Weather Events
Extreme hourly rainfall events
Two events in Lower Ohio
  North in July 2016
  South in August 2016
Big Sandy
  6/24/2017
  Most subs had the higher event in April 2015 (outside calibration period)
Twelvepole
  Does not have the storm spike in the calibration period.
  Large event 7/2017 – after calibration
  Most April 2015
  6/6/2016
  The 17 calibration subs that do have this spike are 3’s and 4’s - unimpaired

## Slide 5: Storm response
1.86” on 8/18
1.44 on 6/24
95% background
Max 400 mg/L

## Slide 6
1.84” on 8/18
1.42” on 6/24
50% disturbed
1,000 mg/L TSS
Storm response

## Slide 7: Storm response
1.58” on 7/29
1.12 on 8/18
50% disturbed
350 mg/L max
Looks like we aren’t getting the same response. However, the 1.58” event is much more like the 1.4” event in previous slide. The amount of sediment increases exponentially with rainfall.

## Slide 8: Subs of note
SWS 4129
  Listed for Fe and pH
  WAB data looks odd
    4 mg/L TSS, 1.7 mg/L Fe (notes describe water as turbid)
    260 mg/L TSS, 6 mg/L Fe
  Mostly undisturbed. Little OOG. Good banks. Low POTFC.
  Are we missing a source?

## Slide 9: Calibration Plots
Fe and TSS

## Slide 10: SWS 725 (Lower Ohio Watershed) 11% Pasture

## Slide 11: SWS 1414 (Big Sandy Watershed) Mixed landuses: 4% Pasture, 9% harvested forest, 2% urban/residential

## Slide 12: SWS 3205 (Twelvepole Watershed) 3% WQ mining, 3% Tech mining, 3% cropland, 4% urban

## Slide 13: SWS 3208 (Twelvepole Watershed) 5% Tech mining

## Slide 14: SWS 3192 (Twelvepole Watershed) 10% WQ Mining, 1% OOG

## Slide 15: SWS 3226 (Twelvepole Watershed) 1% OOG

## Slide 16: SWS 3237 (Twelvepole Watershed) 4% urban/residential

## Slide 17: SWS 4090 (Twelvepole Watershed) 99% background